## Slide 1: Enhancing Cryptographic Application Performance on RISC-V Processors with B and K Extensions
Name: Harsh Dabhi
ID: A00010544
Supervisor : Prof. Xiaojun Wang

## Slide 2: What is the Problem? & Why?
What is the Problem?
Cryptographic algorithms like AES (Advanced Encryption Standard) and SHA (Secure Hash Algorithm) are essential for securing data in modern computing systems. They ensure that sensitive information, such as passwords, financial transactions, and personal data, remains confidential and tamper-proof.
However, these algorithms are computationally intensive. For example:
AES involves multiple rounds of substitutions, shifts, and mixing operations to encrypt data.
SHA performs complex bit-level operations to generate unique hash values for data integrity.
This computational complexity creates challenges in terms of throughput (how fast data can be processed), energy efficiency (how much power is consumed), and resource utilization (how much hardware is required).
Why is There a Problem?
Resource-Constrained Environments: Many modern devices, such as IoT sensors, smartphones, and embedded systems, have limited processing power, memory, and battery life. Running computationally intensive cryptographic algorithms on these devices can lead to:
Slow Performance: Delays in processing data, which can be critical in real-time applications.
High Energy Consumption: Draining battery life quickly, which is a major concern for IoT devices.
Hardware Overhead: Requiring additional hardware resources, which increases cost and complexity.

## Slide 3: Previous Work and Related Solutions
To address the computational complexity of cryptographic algorithms such as AES (Advanced Encryption Standard) and SHA (Secure Hash Algorithm), researchers have explored several approaches
Software-Based Optimizations
Loop Unrolling & Table Lookups: Precomputed tables for AES SubBytes and MixColumns to reduce redundant computations.
SIMD (Single Instruction, Multiple Data): Leverages parallel processing capabilities in general-purpose CPUs.
JIT (Just-in-Time) Compilation: Dynamically optimizes cryptographic operations at runtime.
Hardware-Based Solutions
Dedicated Cryptographic Accelerators: ASICs (Application-Specific Integrated Circuits) optimized for cryptographic tasks, offering high speed but lacking flexibility.
FPGA Implementations: Reconfigurable hardware used to accelerate AES and SHA functions, striking a balance between performance and adaptability.
RISC-V Instruction Set Extensions (B & K): Introduces specialized bitwise and cryptographic instructions directly within the processor, reducing execution cycles and energy consumption.

## Slide 4: RISC-V B & K Extensions Cryptographic Enhancements and Performance Insights
B Extension: Optimizes bit-level operations (e.g., shifts, rotations) critical for AES and SHA.
K Extension: Provides specialized instructions for cryptographic primitives (e.g., AES SubBytes, SHA compression).
Performance Gains: Up to 3x throughput improvement and 30% energy efficiency gains compared to software-only solutions.
Mathematical AES: Based on substitution-permutation networks (SPN), involving matrix transformations, modular arithmetic, and Galois field operations (GF(2^8)).
SHA: Utilizes bitwise logical functions (AND XOR OR), modular addition, and compression functions to transform message blocks into fixed-length digests.

## Slide 5: Comparative Analysis of Approaches
Key Insights from Prior Work
✅ Software-only solutions provide flexibility but lack the efficiency of hardware acceleration.
✅ Instruction set extensions (B & K) offer a balanced solution, leveraging general-purpose processors while integrating cryptographic optimizations.
✅ Proprietary hardware accelerators (ASICs) provide unmatched speed, but are costly and inflexible.
Approach | Flexibility | Speed | Energy Efficiency | Cost
Software-Only | High | Low | Low | Low
Instruction Set Extensions (B & K) | Medium | High | High | Moderate
Dedicated ASICs | Low | Very High | Very High | High

## Slide 6: Proposed Solution Strategy
Leverage Software-Based Optimizations
1.Algorithmic Enhancements
Implement loop unrolling and table-based substitutions to reduce redundant computations in AES encryption.
Use bit-sliced implementations for parallel processing in SHA hash calculations.
2. Parallel Processing with SIMD & Multi-threading
Utilize SIMD (Single Instruction, Multiple Data) instructions to execute cryptographic operations faster.
Enable multi-threading to process multiple encryption/hash operations simultaneously.
3. Code Optimization & Compiler Tuning
Optimize assembly-level code to reduce instruction count.
Use Just-in-Time (JIT) compilation to dynamically adjust execution paths for efficiency.
RISC-V Instruction Set Extensions for Cryptography
1. B Extension (Bit-Manipulation) – Reducing Instruction Complexity
Accelerates bitwise shifts, rotations, and XOR operations.
Speeds up modular arithmetic operations used in AES and SHA.
2. K Extension (Cryptography) – Hardware-Assisted Crypto Primitives
Adds dedicated instructions for AES SubBytes, MixColumns, and AddRoundKey.
Implements SHA message scheduling and compression at the hardware level.
Reduces execution cycles by up to 3x compared to software-only solutions.

## Slide 7: Proposed Solution Strategy
Use RISC-V Simulators to Validate Performance Gains
Spike & QEMU: Measure execution cycles and efficiency with and without extensions.
Gem5 with Power Modeling (McPAT): Evaluate energy consumption of optimized implementations.
Benchmark AES & SHA using real-world workloads (variable key sizes, mixed encryption-decryption).
Comparative Analysis: Software vs. Instruction Set Extensions vs. Proprietary Hardware
Test Case 1: AES encryption with different optimization levels (software-only, B-extension, K-extension).
Test Case 2: SHA hashing throughput comparison across different architectures.
Test Case 3: Power efficiency trade-off analysis for embedded and IoT applications.

## Slide 8: Project Plan for Semester 2 and Summer
March:
Finalize simulation setup and baseline testing for software-only solutions.
1
April:
Implement RISC-V B and K extensions and run initial benchmarks.
2
May:
Compare results with proprietary hardware accelerators.
3
June:
Optimize software implementations and analyze energy efficiency.
4
July:
Design realistic workloads and conduct performance evaluations.
5
August:
Finalize findings and prepare project report.
6

## Slide 9: Conclusion
RISC-V B and K extensions offer a balanced approach, combining software flexibility with hardware acceleration.
The proposed solution focuses on software-centric optimizations with minimal hardware support, providing a cost-effective alternative to proprietary accelerators.
Future work includes experimental validation on physical RISC-V hardware.